## Slide 1
Autonomous robotic manipulator for AMR sampling (Petri Dish)
ELD411
Arnav Panjla 2023EE10978
Manashvi Garg 2023EE11104
Mid-Term Review — 2026

## Slide 2
CONTENTS
Table of contents
01
Problem statement
Village sampling, and the lab bottleneck
02
Market analysis
Planning load, about 1200 dishes a day
03
Hardware iterations
Gantry rejected. SCARA too slow to build
04
Robotic arm and full-system CAD
6-DOF arm, cell layout, link changes
05
Compute platform
Ubuntu first, then Raspberry Pi OS for the HAT
06
Gazebo simulation
Arm motion beside the dish carousel
07
Vision
Circles on the plate, then the antibiotic stamp
08
Progress and roadmap
What is done, and what is left
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 3
PROBLEM STATEMENT
The Challenge: Scaling AMR Surveillance
02
01
VILLAGES
Distributed sampling
02
COLLECTION
Repeated visits
03
LAB
Central processing
04
DISHES
Handling + imaging
05
BOTTLENECK
Manual repetition
Repeated sampling creates high laboratory load.
Dish transport, imaging and logging are repetitive.
Manual handling limits throughput and traceability.
OBJECTIVE
Automate Petri-dish
handling + imaging
IIT Delhi · ELD411 · Mid-Term Review 2026
    Antimicrobial resistance (AMR) requires continuous surveillance.
    Rural/village-level sampling can generate many biological samples.
    Samples need to be collected, transported, incubated/processed and analyzed.
    Manual Petri-dish handling becomes a bottleneck as sample volume increases.

## Slide 4
MARKET AND SCALE ANALYSIS
From Village Sampling to Laboratory Load
03
~3000
people / village
2–3%
sampling fraction*
(people that get sick and actually need testing)
60–90
samples / village
4–5
field collectors
5–6
villages / collector / day
DESIGN TARGET
~1200
PETRI DISHES / DAY
Planning value for workflow, storage and robot duty cycle
ASSUMPTION
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 5
Iteration - I · 3D-printer / gantry frame
04
01
FULL XY GANTRY
Whole frame rides the gantry; nothing moves independently of it.
02
RESTRICTED REACH
Gripper travel is tied to the frame axis — cannot reach every individual dish slot at the carousel.
03
MATERIAL WASTE
Rails sized to the full base footprint even though only the carousel radius is used.
04
VERDICT: REJECTED
Frame motion, not the gripper, was the actual constraint. Scrapped before build.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 6
Iteration - II · SCARA arm
05
01
FULL WORKSPACE REACH
Arm swept the entire carousel; range of motion was exactly enough.
02
HARDER CONTROL MATH
Coupled joint angles replace simple XY moves — more complex than iteration I.
03
FULLY CUSTOM BUILD
Every link had to be designed and 3D-printed from zero — no off-the-shelf part fit.
04
VERDICT: TOO SLOW TO BUILD
Print-fit-reprint cycles on every joint made the build timeline the real blocker.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 7
FULL-PROJECT LAYOUT
Final design · 6-DOF arm replaces the SCARA
06
IIT Delhi · ELD411 · Mid-Term Review 2026
1
1
Frame — aluminium extrusion cell
2
2
Carousel A — dish storage column
3
3
Carousel B — dish storage column
4
4
Robotic arm — 6-DOF (final swap-in)
5
5
Imaging station — staging table
6
6
Control box — drivers / electronics
7
7
Base plate — mounting deck

## Slide 8
MANIPULATOR HARDWARE
6-DOF Robotic Arm
07
IIT Delhi · ELD411 · Mid-Term Review 2026
Elevation · reach check against carousel
Full assembly, dimensioned · 650 × 800 × 525 mm envelope

## Slide 9
MECHANICAL ADAPTATION
Manipulator Modifications for Petri-Dish Reach
08
01
LONGER LINKS
Extend joints so the gripper clears the outer carousel ring
02
CAMERA MOUNT
Rigid mount above gripper, aligned with the QR scan axis (yet to decide)
03
CABLE ROUTING
Slack CSI + power routing so cables survive full joint travel
IIT Delhi · ELD411 · Mid-Term Review 2026
04
WIDER BASE
Widen 2 base-side links so reach stays even across the full carousel span.

## Slide 10
COMPUTE PLATFORM
Raspberry Pi Setup
10
01
UBUNTU SERVER
First OS on the Pi. Chosen because ROS 2 install and packaging is easier on Ubuntu.
02
CAMERA TEST
Camera Module verified working under Ubuntu Server before anything else was built.
03
SWITCH TO RASPBERRY PI OS
Final OS. The add-on HAT board is only supported on Raspberry Pi OS, not Ubuntu.
WHY RASPBERRY PI OS WON
HAT compatibility decided it: the camera/control HAT ships drivers for Raspberry Pi OS only. Ubuntu stayed useful for early ROS 2 experiments, but the deployed board runs Raspberry Pi OS.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 11
VALIDATION
Simulation Recording — Gazebo
11
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 12
VISION
01
INNER DISK + OUTER ZONE
Red = disk. Purple = inhibition zone. Blue = dish rim.
THE ANTIBIOTIC DISKS
Each stamp is a second read. Circles do not give the code.
IIT Delhi · ELD411 · Mid-Term Review 2026
Notes: cicle detection

## Slide 13
STEP 1 · CIRCLES
Before detection
02
INPUT
Raw plate. No circle is drawn yet.
cv2.cvtColor
BGR to gray
cv2.GaussianBlur
gray, (9, 9), 2
Blur is only here so speckle does not become a circle.
IIT Delhi · ELD411 · Mid-Term Review 2026
Notes: low pass = gaussian blur
edge shrapening = canny filter
clahe =
morphology
brightness contrast

## Slide 14
STEP 1 · CIRCLES
After detection
03
01 DISH RIM
cv2.HoughCircles
HOUGH_GRADIENT
Largest circle. Blue.
02 INNER DISK
HoughCircles again
radius 1.6–4.5 mm
Brightness gate. Red.
03 OUTER ZONE
Radial profile
Not Hough
Gray step around the disk. Purple.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 15
STEP 2 · STAMP
Low-pass · Gaussian blur
04
cv2.GaussianBlur(gray, (15, 15), 4)
BEFORE
AFTER · GAUSSIAN BLUR
Low-pass. Agar grain and sensor noise become false edges if they reach Canny or Hough. The plate detector uses the same call at (9, 9), σ = 2.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 16
STEP 2 · STAMP
Edges · Canny
05
cv2.Canny(gray, 20, 60)
BEFORE
AFTER · CANNY
Canny edge detector: Sobel gradient, non-maximum suppression, hysteresis. It returns an edge map, not a character. Thresholds 60 / 160 drop these soft strokes.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 17
STEP 2 · STAMP
Local contrast · CLAHE
06
cv2.createCLAHE(clipLimit=2.0, tileGridSize=(8, 8)).apply(gray)
BEFORE
AFTER · CLAHE
Contrast-limited adaptive histogram equalization. Lifts stamp-versus-paper contrast inside small tiles without blowing the whole crop.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 18
STEP 2 · STAMP
Morphology · opening
07
ker = cv2.getStructuringElement(cv2.MORPH_ELLIPSE, (7, 7)); cv2.morphologyEx(ink, cv2.MORPH_OPEN, ker, iterations=1)
BEFORE · OTSU
AFTER · MORPH OPEN
Opening is erosion, then dilation. Thin arcs break. Thick strokes stay. The binary input is Otsu: cv2.threshold(..., THRESH_OTSU). Still not a string.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 19
STEP 2 · STAMP
Filters were not the reader
09
TRADITIONAL PATH
Another image.
Never the code.
Gaussian blur — smoother pixels
Canny — an edge map
CLAHE — local contrast
Morphology — thinner strokes
convertScaleAbs — brighter paper
GEMMA 3 4B
Reads the disk
in one call.
Local model, gemma3:4b.
No hand-built filter chain on the stamp.
The model does the filtering and the read.
Hough still finds the circles first.
Gemma does not replace that step.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 20
DECISION LEFT OPEN
Two readers, one circle step
10
LOWER COMPUTE
Traditional filters
Gaussian, CLAHE, Canny, morphology, brightness / contrast, then an OCR engine.
Fits the Raspberry Pi.
No large model.
Did not read these rotated stamps.
HIGHER COMPUTE
Gemma 3 4B
One local vision-language call on the disk crop. Filtering and reading happen inside the model.
Heavier than the Pi filter path.
12 / 12 on the upright test1.png crops.
Kept, not locked in.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 21
NATIVE GEMMA + RIM STRIP
12 / 12 on this plate only
10
TEST1
12/12
Eye-read ground truth.
n = 12 is not clinical accuracy.
Offline after
ollama pull gemma3:4b
01
IPM 10
02
TZP 110
03
GM 10
04
MEM 10
05
AN 30
06
CAZ 30
07
SXT
08
NN 10
09
AM 10
10
CRO 30
11
CZ 30
12
CIP 5
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 22
STEP 1 · CIRCLES
Same detector, other plates
11
s2 · AMP, E, NA
s3 · CIP, AMX, AK
s5 · denser plate
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 23
STEP 2 · STAMP
Images in front of the reader
12
test1 · Hough disks
Upright stamps · letters above, digits below
Rim ink stripped · before / after, all 12 disks
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 24
Current Progress & Roadmap
MID-TERM STATUS
Problem & system definition
COMPLETED
Hardware architecture
COMPLETED
Raspberry Pi + camera
COMPLETED
Computer vision pipeline
IN PROGRESS
ESP32 + Zephyr RTOS
IN PROGRESS
Manipulator procurement
IN PROGRESS
Gazebo simulation
IN PROGRESS
Autonomous pick & place
UPCOMING
NEXT PHASE ROADMAP
01
Finalize manipulator
Procurement + end-effector integration
02
Complete perception
Dish localization + feature detection
03
Implement robot control
ESP32 / Zephyr + motor interface
04
Validate in Gazebo
ROS 2 + trajectories + pick/place
05
System integration
Vision → coordinates → manipulation
06
Throughput testing
Target: ~100 dishes/day
Notes: + market analyis
+ Hardware testing
+ failed iterations
+

## Slide 25
THANK YOU