## Slide 1
VISION
Two jobs on one plate
01
INNER DISK + OUTER ZONE
Red = disk. Purple = inhibition zone. Blue = dish rim.
THE ANTIBIOTIC DISKS
Each stamp is a second read. Circles do not give the code.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 2
STEP 1 · CIRCLES
Before detection
02
INPUT
Raw plate. No circle is drawn yet.
cv2.cvtColor
BGR to gray
cv2.GaussianBlur
gray, (9, 9), 2
Blur is only here so speckle does not become a circle.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 3
STEP 1 · CIRCLES
After detection
03
01 DISH RIM
cv2.HoughCircles
HOUGH_GRADIENT
Largest circle. Blue.
02 INNER DISK
HoughCircles again
radius 1.6–4.5 mm
Brightness gate. Red.
03 OUTER ZONE
Radial profile
Not Hough
Gray step around the disk. Purple.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 4
STEP 2 · STAMP
Low-pass · Gaussian blur
04
cv2.GaussianBlur(gray, (15, 15), 4)
BEFORE
AFTER · GAUSSIAN BLUR
Low-pass. Agar grain and sensor noise become false edges if they reach Canny or Hough. The plate detector uses the same call at (9, 9), σ = 2.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 5
STEP 2 · STAMP
Edges · Canny
05
cv2.Canny(gray, 20, 60)
BEFORE
AFTER · CANNY
Canny edge detector: Sobel gradient, non-maximum suppression, hysteresis. It returns an edge map, not a character. Thresholds 60 / 160 drop these soft strokes.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 6
STEP 2 · STAMP
Local contrast · CLAHE
06
cv2.createCLAHE(clipLimit=2.0, tileGridSize=(8, 8)).apply(gray)
BEFORE
AFTER · CLAHE
Contrast-limited adaptive histogram equalization. Lifts stamp-versus-paper contrast inside small tiles without blowing the whole crop.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 7
STEP 2 · STAMP
Morphology · opening
07
ker = cv2.getStructuringElement(cv2.MORPH_ELLIPSE, (7, 7)); cv2.morphologyEx(ink, cv2.MORPH_OPEN, ker, iterations=1)
BEFORE · OTSU
AFTER · MORPH OPEN
Opening is erosion, then dilation. Thin arcs break. Thick strokes stay. The binary input is Otsu: cv2.threshold(..., THRESH_OTSU). Still not a string.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 8
STEP 2 · STAMP
Brightness and contrast
08
cv2.convertScaleAbs(gray, alpha=1.7, beta=12)
BEFORE
AFTER · convertScaleAbs
out = saturate(alpha × pixel + beta). Alpha is contrast. Beta is brightness. Ink separates from the paper. The output is still an image.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 9
STEP 2 · STAMP
Filters were not the reader
09
TRADITIONAL PATH
Another image.
Never the code.
Gaussian blur — smoother pixels
Canny — an edge map
CLAHE — local contrast
Morphology — thinner strokes
convertScaleAbs — brighter paper
GEMMA 3 4B
Reads the disk
in one call.
Local model, gemma3:4b.
No hand-built filter chain on the stamp.
The model does the filtering and the read.
Hough still finds the circles first.
Gemma does not replace that step.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 10
DECISION LEFT OPEN
Two readers, one circle step
10
LOWER COMPUTE
Traditional filters
Gaussian, CLAHE, Canny, morphology, brightness / contrast, then an OCR engine.
Fits the Raspberry Pi.
No large model.
Did not read these rotated stamps.
HIGHER COMPUTE
Gemma 3 4B
One local vision-language call on the disk crop. Filtering and reading happen inside the model.
Heavier than the Pi filter path.
12 / 12 on the upright test1.png crops.
Kept, not locked in.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 11
STEP 1 · CIRCLES
Same detector, other plates
11
s2 · AMP, E, NA
s3 · CIP, AMX, AK
s5 · denser plate
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 12
STEP 2 · STAMP
Images in front of the reader
12
test1 · Hough disks
Upright stamps · letters above, digits below
Rim ink stripped · before / after, all 12 disks
IIT Delhi · ELD411 · Mid-Term Review 2026