## Slide 1
ELD411 · MID-TERM REVIEW 2026
Autonomous Robotic Manipulator for AMR Sampling
Automated Petri Dish Handling, Imaging and Analysis
Arnav Panjla · 2023EE10978 Manashvi Garg · 2023EE1141
Indian Institute of Technology Delhi
01
VILLAGE
02
DISHES
03
ROBOT
04
VISION
05
ANALYSIS

## Slide 2
PROBLEM STATEMENT
The Challenge: Scaling AMR Surveillance
02
01
VILLAGES
Distributed sampling
02
COLLECTION
Repeated field visits
03
LABORATORY
Central processing
04
PETRI DISHES
Imaging + handling
05
BOTTLENECK
Manual repetition
Large-scale AMR surveillance creates repeated biological sampling.
Rural collection feeds a distributed village-to-laboratory workflow.
Laboratory work adds repetitive dish transport, imaging and logging.
Automation targets repeatability, traceability and operator workload.
PROJECT OBJECTIVE
Automate repetitive Petri-dish operations
robotic handling + controlled imaging
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 3
DESIGN SCENARIO
From Village Sampling to Laboratory Load
03
~100
people / village
2–5%
sampling fraction*
2–5
samples / village
4–5
field collectors
5–6
villages / day
DESIGN TARGET
~100
PETRI DISHES / DAY
Planning value for sizing workflow, storage and robot duty cycle
ASSUMPTION
*2–5% is a project design assumption, not an epidemiological estimate.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 4
CAPACITY SIZING
Why a 600-Dish Processing Pipeline?
04
DAY 1
100
in process
DAY 2
200
in process
DAY 3
300
in process
DAY 4
400
in process
DAY 5
500
in process
DAY 6
600
in process
100
dishes / day
×
5–6
days
≈ 500–600
Multiple daily batches remain under observation simultaneously.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 5
SYSTEM ARCHITECTURE
Proposed Autonomous Petri-Dish Processing System
05
PETRI DISH INPUT
CAMERA
RASPBERRY PI 5 CV · LOCALIZATION · PLANNING
ESP32 REAL-TIME CONTROL
MANIPULATOR + END EFFECTOR
IMAGING / STORAGE CAROUSEL
HIGH-LEVEL INTELLIGENCE
DETERMINISTIC CONTROL
Control split
Pi estimates what and where. ESP32 executes when and how.
Feedback closes the loop after grip, transfer and release.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 6
THREE-LAYER STACK
Hardware Selection
06
COMPUTATION
Raspberry Pi 5
Computer vision · planning · system logic
CONTROL
ESP32 / controller
Timing · motor commands · feedback
ACTUATION
Drivers + motors + SCARA
Dish handling · gripping · positioning
01
12 MP CAMERA
Controlled image capture
02
END EFFECTOR
Petri-dish gripping
03
CONTROLLED LIGHT
Repeatable illumination
04
CAROUSEL / STORAGE
Dish queue + controlled chamber
ROUGH POWER ENVELOPE
~95 W typical · ~145 W peak
Estimate only — verify with measured current after hardware integration.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 7
COMPUTE PARTITIONING
Separating Perception from Real-Time Control
07
INTELLIGENCE
Raspberry Pi 5
Computer vision
Image processing
Position estimation
High-level planning
Camera interface
DETERMINISTIC CONTROL
ESP32 + RTOS path
Motor-control timing
Hardware interfaces
Command execution
Limit / feedback inputs
Zephyr evaluation planned
CONTROL COMMANDS
Current repository evidence: ESP32/Arduino prototypes; Zephyr remains an integration target.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 8
MAKE-OR-BUY DECISION
Manipulator Selection & Procurement
08
BUILD FROM SCRATCH
High mechanical effort
01
CAD + fabrication
02
Joint calibration
03
Structural iteration
04
Longer integration path
EVALUATION PATH
Pre-built candidate
Faster prototype start
Focus on vision + control
Known payload / repeatability
ROS 2 / Gazebo support desirable
DECISION OPEN · Pre-built speed vs current custom SCARA BOM
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 9
CURRENT EVIDENCE
Computer Vision for Petri-Dish Analysis
09
01 RAW IMAGE
02 CIRCULAR ROI
03 DETECTION
MEASURE
Dish radius Inhibition-zone radius Feature location
OpenCV baseline
PREPROCESS
DISH DETECT
ROI
ZONE DETECT
MEASURE
OCR*
*OCR for handwritten labels remains planned.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 10
CALIBRATION GEOMETRY
Controlled Petri-Dish Imaging
10
CAMERA
CONTROLLED DISTANCE
PETRI DISH
DIFFUSED LIGHT
DIFFUSED LIGHT
01
FIXED POSITION
Simplifies calibration
02
CONTROLLED LIGHT
Reduces image variation
03
CENTER + RADIUS
Localizes dish geometry
04
ZONE RADIUS
Supports measurement
05
LABEL OCR
Future identification path
Target object: 90 mm plate · 12 MP Camera Module 3 listed in BOM
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 11
PLANNED SIMULATION WORKBENCH
From Robot Description to Gazebo Simulation
11
01
CAD
geometry
02
URDF
joints + links
03
ROS 2
interfaces
04
GAZEBO
world + physics
05
CONTROL
sensors + joints
06
PICK & PLACE
trajectories
SIMULATION VALIDATES
Workspace reach
Joint limits
Trajectory feasibility
Collision behavior
Pick-place sequence
CURRENT STATUS
Architecture defined
No Gazebo model or screenshot exists in repository yet.
Next artifact: URDF + workspace test
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 12
AUTONOMOUS PICK-AND-PLACE
Vision-to-Manipulation Pipeline
12
01
CAPTURE
camera
02
DETECT
dish
03
LOCALIZE
x, y, θ
04
TRANSFORM
camera → robot
05
PLAN
collision-aware
06
APPROACH
pre-grasp
07
GRIP
confirm hold
08
TRANSFER
target pose
09
RELEASE
place dish
10
VERIFY
close loop
PERCEPTION · LOCALIZATION · PLANNING · MANIPULATION · VERIFICATION
Verification prevents silent failures and enables retry / operator escalation.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 13
BOM AND PROCUREMENT EVIDENCE
Prototype Hardware & Bill of Materials
13
COMPONENT
FUNCTION
STATUS
Raspberry Pi 5 · 4 GB
Vision / computation
BOM / SELECTED
Camera Module 3 · 12 MP
Petri-dish imaging
BOM / SELECTED
ESP32-CAM / controller
QR + control prototypes
PROTOTYPE CODE
SCARA manipulator
Dish handling
BOM / DESIGN
5× NEMA17 + drivers
Joint actuation
BOM / DESIGN
End effector + servo
Dish gripping
BOM / DESIGN
Lighting + fixtures
Repeatable imaging
BOM / DESIGN
POWER ENVELOPE
~95 W typical · ~145 W peak
Prices and supplier commitments are not recorded in repository BOM.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 14
MID-TERM STATUS
Current Progress & Roadmap
14
COMPLETED
Problem + system definition
Initial hardware architecture
Pi camera workflow
OpenCV detection baseline
IN PROGRESS
CV robustness + calibration
Manipulator selection
Control-stack decision
BOM finalization
UPCOMING
URDF + Gazebo validation
Vision-to-robot transform
Autonomous pick + place
Throughput testing
NEXT PHASE
01
Finalize manipulator
02
Complete CV calibration
03
Implement control path
04
Validate ROS 2 + Gazebo
05
Integrate vision + arm
06
Test throughput
FINAL TARGET
Autonomous vision-guided Petri-dish handling
~100 DISHES / DAY
IIT Delhi · ELD411 · Mid-Term Review 2026