## Slide 1
Autonomous robotic manipulator for AMR sampling (Petri Dish)
ELD411
Arnav Panjla 2023EE10978
Manashvi Garg 2023EE11104
Mid-Term Review — 2026

## Slide 2
PROBLEM STATEMENT
The Challenge: Scaling AMR Surveillance
02
01
VILLAGES
Distributed sampling
02
COLLECTION
Repeated visits
03
LAB
Central processing
04
DISHES
Handling + imaging
05
BOTTLENECK
Manual repetition
Repeated sampling creates high laboratory load.
Dish transport, imaging and logging are repetitive.
Manual handling limits throughput and traceability.
OBJECTIVE
Automate Petri-dish
handling + imaging
IIT Delhi · ELD411 · Mid-Term Review 2026
  Antimicrobial resistance (AMR) requires continuous surveillance.
  Rural/village-level sampling can generate many biological samples.
  Samples need to be collected, transported, incubated/processed and analyzed.
  Manual Petri-dish handling becomes a bottleneck as sample volume increases.

## Slide 3
MARKET AND SCALE ANALYSIS
From Village Sampling to Laboratory Load
03
~3000
people / village
2–3%
sampling fraction*
(people that get sick and actually need testing)
60–90
samples / village
4–5
field collectors
5–6
villages / collector / day
DESIGN TARGET
~1200
PETRI DISHES / DAY
Planning value for workflow, storage and robot duty cycle
ASSUMPTION
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 4
Iteration - I · 3D-printer / gantry frame
04
01
FULL XY GANTRY
Whole frame rides the gantry; nothing moves independently of it.
02
RESTRICTED REACH
Gripper travel is tied to the frame axis — cannot reach every individual dish slot at the carousel.
03
MATERIAL WASTE
Rails sized to the full base footprint even though only the carousel radius is used.
04
VERDICT: REJECTED
Frame motion, not the gripper, was the actual constraint. Scrapped before build.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 5
Iteration - II · SCARA arm
05
01
FULL WORKSPACE REACH
Arm swept the entire carousel; range of motion was exactly enough.
02
HARDER CONTROL MATH
Coupled joint angles replace simple XY moves — more complex than iteration I.
03
FULLY CUSTOM BUILD
Every link had to be designed and 3D-printed from zero — no off-the-shelf part fit.
04
VERDICT: TOO SLOW TO BUILD
Print-fit-reprint cycles on every joint made the build timeline the real blocker.
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 6
FULL-PROJECT LAYOUT
Final design · 6-DOF arm replaces the SCARA
06
IIT Delhi · ELD411 · Mid-Term Review 2026
1
1
Frame — aluminium extrusion cell
2
2
Carousel A — dish storage column
3
3
Carousel B — dish storage column
4
4
Robotic arm — 6-DOF (final swap-in)
5
5
Imaging station — staging table
6
6
Control box — drivers / electronics
7
7
Base plate — mounting deck

## Slide 7
MANIPULATOR HARDWARE
Selected 6-DOF Robotic Arm
07
IIT Delhi · ELD411 · Mid-Term Review 2026
Elevation · reach check against carousel
Full assembly, dimensioned · 650 × 800 × 525 mm envelope

## Slide 8
MECHANICAL ADAPTATION
Manipulator Modifications for Petri-Dish Reach
08
01
LONGER LINKS
Extend joints so the gripper clears the outer carousel ring
02
CAMERA MOUNT
Rigid mount above gripper, aligned with the QR scan axis
03
CABLE ROUTING
Slack CSI + power routing so cables survive full joint travel
IIT Delhi · ELD411 · Mid-Term Review 2026
04
WIDER BASE
Widen 2 base-side links so reach stays even across the full carousel span.
Notes: new arm drawong wil all dimnesion

## Slide 9
MECHANICAL ADAPTATION
Modified Arm — Dimensioned Drawing
09
+
DROP THE UPDATED ARM DRAWING HERE
2 lengthened base-side links + wider base, with full dimensions
MEASUREMENTS NEEDED
Link 1 — new length (mm)
Link 2 — new length (mm)
Base width — new (mm)
Joint offsets after extension
Updated reach vs carousel radius
Torque check at new lever arm
IIT Delhi · ELD411 · Mid-Term Review 2026

## Slide 10
COMPUTE PLATFORM
Raspberry Pi Setup
10
01
UBUNTU SERVER
First OS on the Pi. Chosen because ROS 2 install and packaging is easier on Ubuntu.
02
CAMERA TEST
Camera Module verified working under Ubuntu Server before anything else was built.
03
SWITCH TO RASPBERRY PI OS
Final OS. The add-on HAT board is only supported on Raspberry Pi OS, not Ubuntu.
WHY RASPBERRY PI OS WON
HAT compatibility decided it: the camera/control HAT ships drivers for Raspberry Pi OS only. Ubuntu stayed useful for early ROS 2 experiments, but the deployed board runs Raspberry Pi OS.
IIT Delhi · ELD411 · Mid-Term Review 2026